## Slide 1
Electrical Workshop
Session One
9/22/2014
Notes: Raphael
- Introduce everyone

## Slide 2: FIRST Power Distribution Diagram

## Slide 3: Power Distribution Diagram
40A
20A
100A
18AWG
18AWG
12AWG
6AWG
Speed Controller

## Slide 4: Battery
12V Lead Acid Battery (18Ah)
13 Pounds
Provides over 100 amperes of current. Total output of over 1200 watts of power.
Can supply over 700 amperes of current when terminals are shorted.

## Slide 5: Robot Power Switch
Used to turn robot on and off
Must be easily accessible
Also a 120 amp circuit breaker

## Slide 6
20-40 Ampere Fuse Locations
Branch circuit power connection
Main Power Connection
Power Distribution Board

## Slide 7: Wires
Wire thickness is based on American Wire Gauge (AWG)
AWG wire thickness is based on the number of wire draws
  Higher gauge = thinner wire
Connection type | Wire Gauge
Battery | 8 AWG
30 - 40A circuit | 12 AWG
20 - 30A circuit | 14 AWG
5 - 20A circuit | 18 AWG
cRIO & Controllers | 18 AWG

## Slide 8: Wire Crimps/Connectors
There are different wire connectors to use depending on what to parts you want to link together.

## Slide 9: Wire Stripping
Wire must be stripped to put on a connector
  Use wire strippers
    Strippers have slots for various gauges. Make sure to check which gauge you wish to strip and use appropriate slot.
  Careful not to cut the wire while stripping
  Make sure to push the handles all the way

## Slide 10: Proper way to put on Crimp
First: strip wire
Second: Slide crimp over the stripped part of the wire
Finally: Using a crimper, squeeze on the crimping area to attach the crimp.

## Slide 11
2013 cRIO; 4 Slots
  Power
    24V Power via PD Board.
  Processor
    400 MHz Freescale MPC5125.
  Memory
    256MB System.
    512MB Storage.
  Cannot provide enough power to control the motors
  So…
The “Brain” of the robot sends control signals to components
Robot Controller CompactRIO National Instruments Embedded Controller
Notes: Servo testers at hobby stores to generate control signal for ESCs
Speaking
Servo is closed loop motor control
Expand ESC
Fix
CPU darkness

## Slide 12
cRIO
Motor/Speed
Controller
Motor
Connections
Copper Wire

## Slide 13: Spike Relays
Relays close or open the circuit based on signals from the cRIO.
Meant for smaller motors

## Slide 14: How an H-Bridge Works
MOTOR
+12V
Ground
S1
S3
S4
S2
S1+S4
FULL FORWARD
S3+S2
FULL REVERSE
S1+S3
BRAKE

## Slide 15: Electric Speed Controllers
Controls the current sent to the motors and the direction the motor turns.
Victor 888 ESC Jaguar ESC Talon ESC
Small, PWM Only
Small, PWM Only
Large, PWM and CAN

## Slide 16: Pulse Width Modulation(PWM)
Pulse Width Modulation is used in two ways on our FIRST Robots:
  To provide a varying amount of power to the motors.
  To communicate with the Speed controller.
ESC
ESC
cRIO
ESC
ESC
ESC
ESC
ESC
ESC

## Slide 17: Controller Area Network(CAN)
“CAN” Stands for “Controller Area Network”
Is a single chain of point-to-point connections
The “bus” goes around the chain delivering the signal to different addresses – each ESC has its own address
2 CAN
ESC
ESC
cRIO
ESC
ESC
ESC
ESC
ESC
ESC
Telephone Wire

## Slide 18: Power Distribution Diagram
40A
20A
100A
18AWG
18AWG
12AWG
6AWG
Speed Controller